Technaxx®  User Manual

Magnet Multi Charger Kit TE09

The Declaration of Conformity is under the Internet link: www.technaxx.de/ (in bottom bar “Konformitätserklärung”); Before using the device, read the user manual carefully.

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks). Free Email: support@technaxx.de

Universal magnetic holder for mobile devices and dual USB Charger

Features

( Magnetic holder for 3.5”~7” mobile devices such as Smartphones and Tablet PCs

( Dual USB charger for the cigarette lighter socket

( Fast and efficient charging with 2.1A

( Short circuit protection

( Flexible gooseneck for different viewing angles

( Mounting with suction cup on plain surfaces

( Wide range of applications: office, kitchen, car, etc.

( Different possibilities to attach the metal plate to the mobile device

IMPORTANT: It is your responsibility to check traffic and safety regulations in your area, to ensure the lawful use of this device.

Technical Specifications

| USB car charger | Output current max. 5V / 2.1A |
| --- | --- |
| Power supply (input power) | DC 12V ~ 24V |
| Output current | max. DC 5V / 2.1A |
| Weight / Dimensions charger | 35g / (L) 9.0 x (W) 4.8 x (H) 4.0cm |
| Weight / Dimensions magnetic holder with metal plate | 43g / (L) 5.5 x (W) 4.0 x (H) 3.0cm |
| Weight / Dimensions gooseneck + suction cup + cap | 112g / (L) 20.5 x Ø 6.5cm of suction cup |
| Weight / Dimensions metal plate | 6g / (L) 5.0 x (W) 3.4 x (H) 0.1cm |
| Package Contents | Dual USB charger, Magnetic holder with flexible gooseneck, 1 metal plate, User Manual |

Charging function

(1) When you charge only in one USB port, the maximum output current is 5V / 2.1A

(2) When you charge in both USB ports at the same time, each USB port output current is then 5V / 1A

Mounting the metal plate – 4 different possibilities

- Attach the adhesive side of metal plate directly to the back of the mobile device.

(2) Attach the adhesive side of metal plate directly to the back of the protection case of your mobile device.

(3) (Large plate only) Attach the adhesive side of metal plate to the interior of the case, between the mobile device and the inside of its case. The plate will adhere to magnetic mount through the rear panel of the case.

NOTE: If choosing not to attach the metal plate to the mobile device or case, leave the adhesive backing of the metal plate in its place. Position the plate between the mobile device and the interior of the case with the metal surface facing the case.

(4) (Small plate only) Similar to option (3), attach the adhesive side of the small plate to the interior of the mobile device rear battery compartment cover (ONLY if space and design permit). Plate will adhere to magnetic mount through rear battery cover.

Mounting the magnetic holder

Attach the magnet to the		Remove the metal plate

mobile device					from the mobile device

Here some examples where to use this magnetic holder

eg. in a car, in the office, in the kitchen, or wherever you have a plain surface.

First clean the surface of the mobile device, before sticking the magnetic holder on it.

Warnings

( Do not attempt to disassemble the charger, it may result in short-circuit or even damage.

( Do not drop, shake or dismantle the charger, it may break internal circuit boards or mechanics.

( Do not expose the charger to an environment with high humidity or high temperature, extensive heat or direct sunlight, moist or underwater conditions.

( Keep the surface of the charger clean, but do not use organic solvents.

( Keep the charger away from little children.

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or solvents/aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany

# Text boxes

When once removed the metal plate from your mobile device, it will not sit tight any longer on another device.

Ball-Joint Adjustment

Flexible Gooseneck