Technaxx®  User Manual

Tablet Car Charger Set TE07

The Declaration of Conformity is under the Internet link: www.technaxx.de/ (in bottom bar “Konformitätserklärung”); Before using the device, read the user manual carefully.

Service phone No. for technical support: 01805 012643 (14 cent/minute from German fixed-line and 42 cent/minute from mobile networks). Free Email: support@technaxx.de

Universal headrest mount for Tablet PCs and dual USB charger

Features

( Universal headrest mount for 7”~11” Tablet PCs

( Dual USB charger for cigarette lighter socket

( Fast and efficiency charging with 2.1A

( Short circuit protection

( Easy to install and remove in all vehicles

IMPORTANT: It is your responsibility to check traffic and safety regulations in your area, to ensure the lawful use of this device.

Technical Specifications

| USB car charger | Output current max. DC 5V / 2.1A |
| --- | --- |
| Power supply (input power) | DC 12V ~ 24V (cigarette ligher socket) |
| Weight / Dimensions charger | 35g / (L) 9.0 x (W) 4.8 x (H) 4.0cm |
| Weight / Dimensions clamp | 86g / (H) 12cm [max. H 19.7cm], (inner W) 7cm, (outer W) 14cm, (Thickness) 5,5cm |
| Weight / Dimensions headrest mount with cap | 85g / (L) 19.8 x (W) 2.5 x (H) 8.5cm |
| Package Contents | Dual USB charger, Headrest mount, Clamp for tablet PC, 1x Cap, User Manual |

Charging function

(1) When you charge only in one USB port, the maximum output current is 5V / 2.1A

(2) When you charge in both USB ports at the same time, each USB port output current is then 5V / 1A

Features of the headrest mount for tablets

( Holder is compatible with 7” ~ 10” Tablet PCs

( Height and angle of the holder is adjustable for best viewing

( Holder supports both, horizontal and vertical viewing

( No need adjust the bracket size again after first use of hold

( Non-slip feet are keeping your mobile device in the holder steadily

( Easy to install and remove in all vehicles

How to assemble the headrest mount

( + ( Place the cap on the end of the gooseneck first.

( Then attach the holder to the end of the gooseneck. You will hear a loud ”click” tone once the holder rested in and is secure. After that tighten the cap to the holder by spinning it to the right.

Install the headrest mount to the headrest rods

Adjust the mount to the correct size

How to remove your tablet PC from the mount

Warnings

( Do not attempt to disassemble the charger, it may result in short-circuit or even damage.

( Do not drop, shake or dismantle the charger, it may break internal circuit boards or mechanics.

( Do not expose the charger to an environment with high humidity or high temperature, extensive heat or direct sunlight, moist or underwater conditions.

( Keep the surface of the charger clean, but do not use organic solvents.

( Keep the charger away from little children.

Hints for Environment Protection: Packages materials are raw materials and can be recycled. Do not disposal old devices or batteries into the domestic waste. Cleaning: Protect the device from contamination and pollution (use a clean drapery). Avoid using rough, coarse-grained materials or solvents/aggressive cleaner. Wipe the cleaned device accurately. Important Notice: Should battery fluid leak from a battery, wipe the battery case with a soft cloth dry. Distributor: Technaxx Deutschland GmbH & Co.KG, Kruppstr. 105, 60388 Frankfurt a.M., Germany

# Text boxes

Fasten and lock on the clamp on the rods with the two click closures.

Adjust the width of the two fasteners to the distance of the rods on rear seat headrest.

Move your tablet PC in the two arrows direction to take it out of the clamp of the headrest mount.

( Turn switch as arrow 1 direction and push the holder vertically as arrow 2 direction.

( Put your tablet PC as arrow 1 and 2 direction. Press the holder down vertically. Make sure your tablet PC hold firmly. Then turn off the switch on the back of the holder.